## Slide 1: IPv6 over Link-Local Discovery Protocol
draft-richardson-anima-ipv6-lldp
M. Richardson
Liang Xia
Jie Yang(presenting)
IETF 107, ANIMA

## Slide 2
Discovery of adjacent systems
Internet
Pledge
(IDevID)
Join Proxy
MASA
“Domain” components
Domain Registrar
(PKI RA)
Key Infrs.
(e.g. PKI CA)
BRSKI-EST
e.g. RFC7030
BRSKI-MASA
Voucher
(RFC 8366)
The pledge talk to Join Proxy using IPv6 Link-Local Address
  On the ACP, Need hop-to-hop discovery of adjacent system
But it is Campus L2 systems
Discovery:
over IPv6 Link-local

## Slide 3
Bootstrap Interlocking Problem
Stable SDN connection can provided by RFC8368.
  (RFC8368 : Using an Autonomic Control Plane for Stable Connectivity of Network Operations, Administration, and Maintenance (OAM))
But before the connection, Broadcast in this Campus L2 systems, => Loop
  Need additional mechanism for Loop-breaking
  Like STP …
    But Can’t automatically configure during on-boarding process

## Slide 4
Proposed LLDP Solution
LLDP(Link Layer Discovery Protocol) Description:
  Standard Layer-2 discovery protocol in IEEE 802.1ab, without Control Plane
  Does not forward packets with default, that is : it discovers all compliant layer-2 devices in a network, even if they do not normally do layer-3 forwarding
About LLDP frames:
  Be sent to the control plane processor, -> exactly the desired for ACP: all traffic goes to the control plane processor.

## Slide 5
LLDP Protocol Encapsulation and issues
About 507 octets limit of vendor-specific frame:
  And the minimum MTU in IPv6 protocol : 1280
  So LLDP IPv6 fragment contain more than one TLV, accommodate up to 1500bytes(often larger…) in Ethernet network
Issue of Subtype TLV values: which better?
  Option-1: Multiple different subtype values
  Option-2: Repeatedly same subtype TLV values
    How to keep the correct order?
Issue of Content payload : which option?
  Option-1: entire IPv6 packet
  Option-2: elided IPv6 packet
  Option-3: compressed packet, RFC8138 or others?
Vendor-specific TLV : 127
TBD
IPv6 fragment : up to 507 octets
IANA unique

## Slide 6
Thank You!